## Slide 1
Supply:Truck-only 44.8→Coordinated 37.5 min
Evac:Full resource 9.1%·No subway 2.8%
Evac:No helicopter 9.0%·Double ambulance 9.2%
Drone-only:infeasible (payload limit)
Double drones:no marginal gain (not bottleneck)
Phase I
Multi-Source Data Integration
Phase II
Incident Scenario Construction
Phase III
Coordinated Optimization
Phase IV
Resilience Assessment
Phase V
Conclusions & Implications
OSM Road Network
Road class · Speed limit · Direction
Baidu POI Database
Hospitals · Fire Stations · Shelters · Subway
National Census (2020)
Age-sex distribution (district level)
Mobile Signaling Data
OD flows · Commute patterns · Mode split
Block-Level Population
Baidu LBS resident distribution
Administrative Boundary
Yizhuang master plan · 15km buffer
Data Processing Pipeline
• BD-09 → GCJ-02 → WGS84 coordinate transformation
• Road clipping → NetworkX digraph → Dijkstra travel time
• Population disaggregation (census age block pop.)
• Subway topology · OD/commute clipping · POI classification
Data Integration & Consistency Check
Spatial overlay · Topology validation · Scenario parameter export
Gaussian Plume Dispersion Model
Cl₂ release 5 kg/min · Wind 3 m/s · Class D stability
Pasquill-Gifford params · Briggs urban formula
C(x,y) = Q/(2πuσyσz) · exp(-y²/2σy²) · ...
ERPG Hazard Zone Classification
Core Zone ERPG-3 (≥20 mg/m³) Immed
Alert Zone ERPG-2 (≥3 mg/m³) Urgent
Buffer Zone ERPG-1 (≥1 mg/m³) Shelter
Road Closure & Congestion Modeling
500m road closure · 1km core closure (96.7 km)
Closure ratio: 19.1% (96.7/505.3 km)
Wind Direction Sensitivity Analysis
Four scenarios: SW(225°) base · N(0°) · E(90°)
Affected Population Classification
k=1 Critical(2%) · k=2 Vulnerable(27%) · k=3 General(71%)
Emergency Supply Delivery Optimization (Step 10) — Centripetal Flow
Three-Tier Logistics Network
Supply (H): 8 fire stations + 2 depots
Transit (I): 5 large-capacity facilities
Demand (J): 15 locations
Four Priority Time Windows
Life rescue 30min (hard)
Medical 60min (hard)
Protection 120min (soft)
Basic supply 240min (soft)
Truck–Drone Coordination
Direct: truck→demand (20 trucks)
Relay: truck→transit→drone (10 UAVs)
Drone: 60km/h · ≤25kg · ≤15km range
Solution Method
Priority-based greedy + 2-opt local search · Dijkstra
Objective Function
min Z = w₁·Makespan + w₂·Σpenalty + w₃·Σunmet
Results: Makespan 44.8→37.5 min (↓16.3%) · Zero penalty · 100% life-res
Multi-Type Personnel Evacuation Optimization — Centrifugal Flow
Five Transport Modes
Ambulance 15 (cap.3) · Helicopter 3 (cap.6)
Subway 5 trains (cap.500) ← backbone
Three Vulnerability Classes
k=1 Critical (ω=10) → Hospital
k=2 Vuln.(ω=5)→Hosp./Shel.
k=3 General(ω=1)→Any shelter
Risk-Aware Dispatch Model
Time-stepping (Δt=5min, T=180min)
Dynamic risk exposure from plume field
Dijkstra on damaged road network
Objective Function
Results: Evacuation rate 9.1%
Finding: Subway = 69% capacity (critical) · Severe capacity gap · Layered strategy
Supply–Evacuation Triple Coupling
① Resource competition: shared damaged network ② Temporal coupling: supply-first → concurrent
evacuation ③ Spatial interaction: centripetal (supply) vs centrifugal (evac.)
Structural Resilience
Road closure ratio: 19.1% (96.7/505.3 km)
Overall network connectivity preserved
Ground delivery remains feasible
Functional Resilience
Supply completion rate: 100%
Evacuation completion rate: 9.1%
⚠ Asymmetry: high supply vs low evac. resilience
Adaptive Resilience
Drone coordination: Makespan ↓16.3%
Subway emergency ops → evac. rate ×3.3
Multi-modal synergy confirmed
Scenario Comparison
Policy Implications & Outlook
Policy Recommendations
❶ Subway emergency operation protocol
(contributes 69% evac. capacity)
❷ Layered evacuation strategy
(1km forced evac. + 1-3km shelter-in-place)
❸ Pre-position helicopters at high-risk corridors
(rapid critical patient transfer)
❹ Invest in UAV infrastructure
(advantage grows with larger disruptions)
❺ Integrate real-time wind monitoring
(dynamic hazard zone updates)
Limitations
• Greedy heuristic: no global optimality
• Uniform age structure at district level
• Static Gaussian plume (not CFD)
• BPR static congestion (no DTA feedback)
Future Directions
• MIP exact methods / ALNS metaheuristic
• CFD-coupled dispersion simulation
• Meso/micro traffic simulation coupling
• Building-level population model
• Calibration with real emergency plans
min Z₁(weighted evac. time) + Z₂(dynamic risk exposure) + Z₃(unserved penalty)
No subway→2.8% · Double ambulance→9.2% · Risk↓4.8%

## Slide 2
第一阶段
多源数据融合
第二阶段
事故场景构建
第三阶段
协同优化求解
第四阶段
韧性评估
第五阶段
结论与建议
OSM路网数据
道路等级 · 限速 · 通行方向
26,699路段 / 11,232 km
百度POI数据库
医院 · 消防站 · 避难所 · 地铁站
25,276个兴趣点
七普人口数据
分年龄·性别人口 (区县级)
老人15% · 儿童12%
百度手机信令
OD流量 · 通勤模式 · 方式划分
5659万日OD / 311.8万通勤
地块级人口数据
百度LBS常住人口分布
地块级空间精度
行政边界数据
亦庄控规界 · 15km缓冲区
研究范围 707 km²
数据处理流水线
• BD-09 → GCJ-02 → WGS84 坐标转换
• 路网裁剪 → NetworkX有向图 → Dijkstra行程时间
• 人口空间分配（七普年龄结构 × 地块级人口）
• 地铁网络拓扑 · OD/通勤数据裁剪 · POI筛选分类
数据整合与一致性检验
空间叠加 · 拓扑检查 · 场景参数输出
高斯烟羽扩散模型
Cl₂泄漏 5 kg/min · 风速 3 m/s · D级稳定度
Pasquill-Gifford扩散参数 · Briggs城市公式
C(x,y) = Q/(2πuσyσz) · exp(-y²/2σy²) · ...
ERPG危险区域三级划分
核心危险区 ERPG-3 (≥20 mg/m³) 立即疏散
警戒区 ERPG-2 (≥3 mg/m³) 紧急疏散
影响区ERPG-1 (≥1 mg/m³) 就地避难
道路封闭与拥堵模拟
500m道路封闭区 · 1km核心封闭区（96.7 km）
3km BPR拥堵区 (α=0.15, β=4.0) · 5km影响区
封闭率 19.1%（96.7/505.3 km）
风向敏感性分析
四种风向：SW(225°)基准 · N(0°) · E(90°)
强SW(225°, 8m/s) → 实时气象融合
受影响人口分类
k=1 重伤(2%) · k=2 脆弱(27%) · k=3 一般(71%)
3km区域总影响口 ≈ 23.5万人
应急物资配送优化— 向心流
三层物流网络
供应点(H): 8消防站+2仓库
中转站(I): 5大容量设施
需求点(J): 15个位置
四级优先级时间窗
生命救援 30min(硬)
医疗支援 60min(硬)
防护设备 120min(软)
基础保障 240min(软)
货车—无人机协同
直送: 货车→需求点 (20辆)
接力: 货车→中转站→无人机 (10架)
无人机: 60km/h · ≤25kg · ≤15km
求解方法
优先级贪心构造 + 2-opt局部搜索 · Dijkstra路网行程时间
目标函数
min Z = w₁·Makespan + w₂·Σpenalty + w₃·Σunmet
结果: Makespan 44.8→37.5 min (↓16.3%) · 零惩罚 · 生命救援100%准时
多类型人员救援疏散优化—离心流
五种交通方式
救护车 15辆(3人) · 直升机 3架(6人)
公交车 20辆(50人) · 私家车 100辆(4人)
地铁 5列(500人/列) ← 疏散主力
贡献69%疏散运力
三类脆弱性分级
k=1重伤中毒(ω=10) →医院
k=2老人儿童(ω=5)→医院/庇护所
k=3一般人员(ω=1)→任意庇护所
加权优先级保护脆弱群体
风险感知调度模型
时间步进式 (Δt=5min, T=180min)
高斯浓度场动态风险暴露
Dijkstra受损路网最短路径
车辆循环调度（含返回时间）
目标函数
min Z₁(加权疏散) + Z₂(动态风险) + Z₃(未服务惩罚)
结果: 疏散率 9.1% (21,312/234,502人)
无地铁→2.8% · 加倍救护车→9.2% · 风险↓4.8%
发现: 地铁贡献69%运力(关键) · 运力严重不足 · 建议分层疏散(1km强制+1-3km就地避难)
物资配送—人员疏散 三重耦合关系
① 资源竞争: 共享受损路网与交通走廊 ② 时间耦合: 物资先行保障→疏散同步展开
③ 空间交互: 向心(配送)与离心(疏散)流向互锁
结构韧性
道路封闭率 19.1% (96.7/505.3 km)
路网整体连通性保留
地面配送仍可行
功能韧性
物资配送完成率: 100%
生命救援准时率: 100%
人员疏散完率: 9.1%
⚠ 不对称特征: 物资高韧性 vs 疏散低韧性
适应韧性
无人机协同 Makespan ↓16.3%
地铁应急运营 → 疏散率×3.3
多模式协同效益已验证
方案对比分析
配送: 纯货车 44.8min → 协同 37.5min
疏散: 全资源 9.1% · 无地铁 2.8%
疏散: 无直升机 9.0% · 加倍救护车 9.2%
无人机: 纯无人机不可行(载重限制)
加倍无人机: 无额外改善(瓶颈非数量)
政策建议与展望
政策建议
❶ 建立地铁应急运营预案
(贡献69%疏散能力)
❷ 分层疏散策略
(1km强制疏散 + 1-3km就地避难)
❸ 高风险走廊预置直升机
(重伤人员快速转运)
❹ 投资无人机基础设施
(大范围破坏时优势凸显)
❺ 实时风向监测整合
(动态更新危险区域)
研究局限
• 贪心启发式不保证全局最优
• 人口年龄结构区县级均匀假设
• 静态高斯烟羽(非CFD)
• BPR静态拥堵(非动态交通流)
未来方向
• MIP精确方法 / ALNS元启发式
• CFD耦合扩散模拟
• 中微观交通仿真耦合
• 建筑级人口模型
• 实际应急预案数据标定

## Slide 3
Phase I
Multi-Source Data Integration
Phase II
Incident Scenario Construction
Phase III
Coordinated Optimization
Phase IV
Resilience Assessment
Phase V
Conclusions & Implications
OSM Road Network
Road class · Speed limit · Direction
26,699 segments / 11,232 km
Baidu POI Database
Hospitals · Fire Stations · Shelters · Subway
25,276 Points of Interest
National Census (2020)
Age-sex distribution (district level)
Elderly 15% · Children 12%
Mobile Signaling Data
OD flows · Commute patterns · Mode split
56.59M daily OD / 3.12M commute
Block-Level Population
Baidu LBS resident distribution
Block-level spatial precision
Administrative Boundary
Yizhuang master plan · 15km buffer
Study area 707 km²
Data Processing Pipeline (Steps 0–7)
• BD-09 → GCJ-02 → WGS84 coordinate transformation
• Road clipping → NetworkX digraph → Dijkstra travel time
• Population disaggregation (census age block pop.)
• Subway topology · OD/commute clipping · POI classification
Data Integration & Consistency Check (Step 8)
Spatial overlay · Topology validation · Scenario parameter export
Gaussian Plume Dispersion Model
Cl₂ release 5 kg/min · Wind 3 m/s · Class D stability
Pasquill-Gifford params · Briggs urban formula
ERPG Hazard Zone Classification
Core Zone ERPG-3 (≥20 mg/m³) Immediate evacuation
Alert Zone ERPG-2 (≥3 mg/m³) Urgent evacuation
Buffer Zone ERPG-1 (≥1 mg/m³) Shelter-in-place
Road Closure & Congestion Modeling
500m road closure · 1km core closure (96.7 km)
3km BPR congestion (α=0.15, β=4.0) · 5km impact zone
Closure ratio: 19.1% (96.7/505.3 km)
Wind Direction Sensitivity Analysis
Four scenarios: SW(225°) base · N(0°) · E(90°)
Strong SW(225°, 8m/s) → Real-time met. integration
Affected Population Classification
k=1 Critical(2%) · k=2 Vulnerable(27%) · k=3 General(71%)
3km zone total affected pop. ≈ 234,502
Emergency Supply Delivery Optimization (Step 10) — Centripetal Flow
Three-Tier Logistics Network
Supply (H): 8 fire stations + 2 depots
Transit (I): 5 large-capacity facilities
Demand (J): 15 locations
Four Priority Time Windows
Life rescue 30min (hard)
Medical 60min (hard)
Protection 120min (soft)
Basic supply 240min (soft)
Truck–Drone Coordination
Direct: truck→demand (20 trucks)
Relay: truck→transit→drone (10 UAVs)
Drone: 60km/h · ≤25kg · ≤15km range
Solution Method
Priority-based greedy + 2-opt local search · Dijkstra network routing
Objective Function
min Z = w₁·Makespan + w₂·Σpenalty + w₃·Σunmet
Results: Makespan 44.8→37.5 min (↓16.3%) · 40/40 tasks completed · Zero penalty · 100% life-rescue on-time
Multi-Type Personnel Evacuation Optimization (Step 11) — Centrifugal Flow
Five Transport Modes
Ambulance 15 (cap.3) · Helicopter 3 (cap.6)
Bus 20 (cap.50) · Private car 100 (cap.4)
Subway 5 trains (cap.500) ← backbone
Contributes 69% of evacuation capacity
Three Vulnerability Classes
k=1 Critical (ω=10) → Hospital
k=2 Vulnerable (ω=5) → Hosp./Shelter
k=3 General (ω=1) → Any shelter
Weighted priority protects the vulnerable
Risk-Aware Dispatch Model
Time-stepping (Δt=5min, T=180min)
Dynamic risk exposure from plume field
Dijkstra on damaged road network
Vehicle recycling (incl. return time)
Objective Function
min Z₁(weighted evac. time) + Z₂(dynamic risk exposure) + Z₃(unserved penalty)
Results: Evacuation rate 9.1% (21,312/234,502)
No subway→2.8% · Double ambulance→9.2% · Risk↓4.8%
Finding: Subway = 69% capacity (critical) · Severe capacity gap · Layered strategy recommended
Supply–Evacuation Triple Coupling
① Resource competition: shared damaged network ② Temporal coupling: supply-first → concurrent evacuation ③ Spatial interaction: centripetal (supply) vs centrifugal (evac.)
Structural Resilience
Road closure ratio: 19.1% (96.7/505.3 km)
Overall network connectivity preserved
Ground delivery remains feasible
Functional Resilience
Supply completion rate: 100%
Life-rescue on-time rate: 100%
Evacuation completion rate: 9.1%
⚠ Asymmetry: high supply vs low evac. resilience
Adaptive Resilience
Drone coordination: Makespan ↓16.3%
Subway emergency ops → evac. rate ×3.3
Multi-modal synergy confirmed
Scenario Comparison
Supply: Truck-only 44.8 → Coordinated 37.5 min
Evac: Full resource 9.1% · No subway 2.8%
Evac: No helicopter 9.0% · Double ambulance 9.2%
Drone-only: infeasible (payload limit)
Double drones: no marginal gain (not bottleneck)
Policy Implications & Outlook
Policy Recommendations
❶ Subway emergency operation protocol
(contributes 69% evac. capacity)
❷ Layered evacuation strategy
(1km forced evac. + 1-3km shelter-in-place)
❸ Pre-position helicopters at high-risk corridors
(rapid critical patient transfer)
❹ Invest in UAV infrastructure
(advantage grows with larger disruptions)
❺ Integrate real-time wind monitoring
(dynamic hazard zone updates)
Limitations
• Greedy heuristic: no global optimality
• Uniform age structure at district level
• Static Gaussian plume (not CFD)
• BPR static congestion (no DTA feedback)
Future Directions
• MIP exact methods / ALNS metaheuristic
• CFD-coupled dispersion simulation
• Meso/micro traffic simulation coupling
• Building-level population model
• Calibration with real emergency plans
Study Context
Coordinated Emergency Supply Distribution and Multi-Type Personnel Evacuation Optimization for HazMat Incidents on Urban Expressways
Incident: Taipingqiao interchange, 6th Ring Rd (116.494°E, 39.736°N) · Agent: Cl₂ · Study area: 15km buffer (707 km²) · Core: Yizhuang Economic-Technological Dev. Area
Legend
Data
Scenario
Supply
Evacuation
Resilience
Analysis flow
Coupling
Key Methods
BD09→WGS84
NetworkX
Gaussian Plume
ERPG
BPR Function
Dijkstra SP
Greedy + 2-opt
Time-Step Dispatch
3D Resilience Eval.

## Slide 5
1. Data Foundation & Preprocessing
Study Area Definition
• Yizhuang regulatory boundary
• 15 km buffer zone
• Incident point annotation
• ~707 km² study area
Step 0
Road Network
• OSM road clipping
• Class / speed / capacity
• NetworkX topology graph
• 26,699 road segments
Step 2
POI Filtering
• Hospitals / fire stations
• Shelters / subway stations
• Vulnerability-sensitive
facilities (schools, etc.)
Step 3
Population Data
• Block-level (Baidu LBS)
• Census age structure
• Vulnerable group ratios
• Spatial join to blocks
Step 4
OD / Commute / Travel
• BD09→WGS84 transform
• OD data clipping
• Dijkstra travel-time matrix
• Subway network topology
Step 5, 6, 7
Data Integration & Consistency Check → Scenario Parameter File (Step 8)
Data Sources
OSM | Baidu LBS | Census
POI | Regulatory Boundary
Key Tools
GeoPandas | NetworkX
Dijkstra | KDTree
Outputs
Road graph | Facility SHP
Population grid | OD matrix
2. Incident Scenario Construction
Gaussian Plume Dispersion & Hazard Zone Delineation (Step 9)
Gaussian Plume Model
• Chlorine leak: Q = 5,000 mg/s
• Wind: u = 3 m/s, dir = 225°
• Atmospheric stability: Class D
• C(x,y) = Q/(2πuσ_yσ_z)·exp(...)
Concentration field → ERPG thresholds
Hazard Zone Delineation
1km
500 m road closure zone
1 km core closure (96.7 km roads)
3 km congestion zone (BPR)
5 km impact zone
ERPG-1/2/3 classification
Impact Assessment
• Affected pop.: ~234,502
• Road closure rate: 19.1%
• Affected facility statistics
• Wind sensitivity (4 dirs)
Time-varying, by population type
Wind Sensitivity
• SW 225° (baseline)
• N 0° / E 90°
• SW 225° strong (8 m/s)
→ Directional sensitivity
→ Real-time met. needed
Resource Competition · Time Coupling · Spatial Interaction
3a. Emergency Supply Delivery
Truck–Drone Cooperative Optimization (Step 10)
← Centripetal
Three-Tier Logistics Network
Supply (H): 8 fire stations + 2 depots
Relay (R): Drone launch pads
Demand (D): Emergency nodes in 5 km
4 supply categories, differentiated TW
Truck–Drone Cooperation
Direct: Truck → Demand point
Relay: Truck → Relay → Drone
BPR congestion: α=0.15, β=4.0
Network Dijkstra travel time
Two-Phase: Greedy Construction + 2-opt Local Search
Obj: min Z = w₁·Makespan + w₂·Σpenalty + w₃·Σunmet
Priority sort → Vehicle-route eval → Local improve → Feasibility
Key Results
✓ 40 tasks 100% completed | Makespan: 44.8 → 37.5 min (↓16.3%)
✓ Life-rescue within 30 min | 39 direct + 1 relay | Drone-only infeasible
Drone sensitivity analysis: 0–40 drones
3b. Multi-Type Evacuation
Priority-Based Scheduling Optimization (Step 11)
Centrifugal →
Three Population Classes
k=1 Critical (ω=10) → Hospital
k=2 Vulnerable (ω=5) → Hosp./Shelter
k=3 General (ω=1) → Shelter
Baidu LBS + Census age ratios
Multi-Modal Fleet
Ambulance (15) | Bus (20)
Helicopter (3) | Subway (Yizhuang)
Private car (commute ratio-based)
Network Dijkstra travel time
Time-Stepped Scheduling (Δt = 5 min, T = 180 min)
min Z = Z₁(weighted time) + Z₂(dynamic risk) + Z₃(unmet penalty)
Priority dispatch → Risk interpolation → Vehicle assign → Capacity check
Key Results
✓ Baseline: 21,312 evacuees (9.1%) | Subway contributes 69%
✓ No-subway drops to 2.8% | Helicopter reduces critical-patient risk
Scenarios: Baseline / No-subway / No-helicopter / Double-ambulance
Coupling
4. Resilience Assessment & Comprehensive Analysis
Three-Dimensional Resilience Framework (Step 12)
Three-Dimensional Framework
Structural
Functional
Adaptive
Structural: 19.1% road closure rate
Functional: Supply 100% | Evac. 9.1%
Adaptive: Drone improvement 16.3%
Core Finding: Asymmetric Resilience
• Supply: High resilience (100%, within 30 min)
• Evacuation: Vulnerability (9.1%, capacity gap)
• Root cause: Task scale disparity (40 vs 234.5k)
Policy Recommendations
① Subway emergency protocol (69% capacity)
② Tiered evac.: core mandatory + shelter-in-place
③ Drone infrastructure ④ Real-time met. integration
Dual Strategy: Mandatory evacuation within 1 km core + Shelter-in-place with PPE at 1–3 km → Manageable demand level
Fig. X Technical Roadmap
Coordinated Emergency Supply Delivery and Multi-Type Personnel Evacuation Optimization
for Hazardous Material Incidents on Urban Expressways — A Case Study of Beijing 6th Ring Road
Legend:
Data Processing
Scenario
Supply (Centripetal)
Evacuation (Centrifugal)
Resilience
Process flow
Coupling relation
Phase boundary
Step 0–12: Code module identifiers

## Slide 6
1. 数据基础与预处理
Data Foundation & Preprocessing
研究范围界定
• 亦庄控规界
• 15km缓冲区
• 事故中心点标注
Step 0
路网处理
• OSM路网裁剪
• 等级/限速/通行能力
• NetworkX拓扑图
Step 2
POI筛选
• 医院/消防站
• 避难场所/地铁站
• 脆弱性设施
Step 3
人口数据
• 地块级人口（百度LBS）
• 七普年龄结构
• 脆弱人群比例估算
Step 4
OD/通勤/行程时间
• BD09→WGS84坐标转换
• OD数据裁剪与统计
• Dijkstra行程时间矩阵
Step 5, 6, 7
数据整合与一致性检验 → 场景参数文件 (Step 8)
数据源
OSM | 百度LBS | 七普
POI | 亦庄控规界
关键工具
GeoPandas | NetworkX
Dijkstra | KDTree
输出产品
路网图 | 设施SHP
人口栅格 | OD矩阵
2. 事故场景构建
Incident Scenario Construction (Step 9)
高斯烟羽扩散模型
• 氯气泄漏: Q=5000 mg/s
• 风速u=3 m/s, 风向225°
• 大气稳定度 D 级
• C(x,y) = Q/(2πuσ_yσ_z)·exp(...)
浓度场计算 → ERPG阈值
危险区域划分
1km
500m 道路封闭区
1km 核心封闭区(96.7km路段)
3km 拥堵区(BPR拥堵)
5km 影响区
ERPG-1/2/3 分级
影响评估
• 受影响人口: ~234,502人
• 路段封闭率: 19.1%
• 受影响设施统计
• 风向敏感性(4方向)
分时段·分类人群估算
风向敏感性分析
• SW 225° (基准)
• N 0° / E 90°
• SW 225° 强风(8m/s)
→ 危险区域方向敏感
→ 需实时气象融入
资源竞争 · 时间耦合 · 空间交互
3a. 应急物资配送优化
Emergency Supply Delivery (Step 10)
← 向心流
三层物流网络
供应点层(H): 8消防站+2仓库
中转站层(R): 无人机起降点
需求点层(D): 5km内应急节点
4类物资·差异化时间窗
货车—无人机协同机制
直送模式: 货车 → 需求点
接力模式: 货车 → 中转站 → 无人机
BPR拥堵: α=0.15, β=4.0
路网Dijkstra行程时间
两阶段求解: 贪心构造 + 2-opt局部搜索
目标: min Z = w₁·Makespan + w₂·Σpenalty + w₃·Σunmet
优先级排序 → 车辆-路径评估 → 局部改进 → 可行性检查
关键结果
✓ 40项任务100%完成 | Makespan: 44.8→37.5 min (↓16.3%)
✓ 生命救援类30min内送达 | 39直送+1接力 | 纯无人机不可行
无人机敏感性分析: 0-40架
3b. 多类型人员疏散优化
Multi-Type Evacuation (Step 11)
离心流 →
三类人群分级
k=1 重伤/中毒(ω=10) → 医院
k=2 老人/儿童(ω=5) → 医院/避难所
k=3 一般人员(ω=1) → 避难所
百度LBS + 七普年龄比例
多模式交通工具
救护车(15辆) | 公交车(20辆)
直升机(3架) | 地铁(亦庄线等)
私家车(通勤驾车比例动态调整)
路网Dijkstra行程时间
时间步进式调度算法 (Δt=5min, T=180min)
min Z = Z₁(加权时间) + Z₂(动态风险暴露) + Z₃(未疏散惩罚)
优先级调度 → 实时风险插值 → 车辆分配 → 避难所容量检查
关键结果
✓ 基准方案疏散21,312人(9.1%) | 地铁贡献69%疏散能力
✓ 无地铁方案骤降至2.8% | 直升机降低重伤人员风险暴露
方案对比: 基准/无地铁/无直升机/加倍救护车
耦合
4. 韧性评估与综合分析
Resilience Assessment & Comprehensive Analysis (Step 12)
三维韧性评估框架
结构
功能
适应
结构韧性: 路网封闭率19.1%
功能韧性: 物资100% | 疏散9.1%
适应韧性: 无人机改善16.3%
核心发现: 不对称韧性特征
• 物资配送: 高韧性(100%完成, 30min内送达)
• 人员疏散: 脆弱性(9.1%完成, 运力严重不足)
• 根源: 任务规模差异(40项 vs 23.5万人)
政策建议
① 地铁应急预案(贡献69%疏散能力)
② 分层疏散: 核心区强制+外围就地避难
③ 无人机基础设施 ④ 实时气象融合
双策略方案: 1km核心区强制疏散 + 1-3km警戒区就地避难配发防护 → 将疏散需求降至可管理水平
图X 技术路线图
城市快速路危险品车辆事故场景下的应急物资配送与多类型人员救援疏散协同优化研究
Fig. X Technical roadmap for coordinated emergency supply delivery and multi-type personnel evacuation optimization
under hazardous material incidents on urban expressways
图例:
数据处理
场景构建
物资配送(向心流)
人员疏散(离心流)
韧性评估
流程方向
耦合关系
阶段边界
Step 0-12: 对应代码模块编号